Stitch quality checking at needle point

---
Application scenario
Application scenario
- Computer vision based solution to automate the process of checking the quality of the stitches according to the standards
- Detect stitch quality as early as possible, that is at needle point of the sewing machine.
- If quality of the stitch is low, it should be notified to the team member who is using this machine

---
Define problem
Define problem
Identify the key types of defects used to measure quality of the stitches.
1. Slipped or skipped stitch
2. Staggered stitch
3. Unbalance stitch
4. Variable stitch
5. Thread breakage etc.
- Build a machine learning model to detect the defects of a given cloth.
- Train the model.
- Implement the system with a raspberry pie and a camera.
- Build the method to notify the team member

---
Existing solutions
Existing solutions
Stitch quality monitoring system for sewing machines - 1996
By Robert N. Cox, Timothy G. Clapp, Kimberly J. Titus
Stitch quality monitoring system for use in combination with a sewing machine having one or more stitch threads and comprising sensor means for at least one of said one or more stitch threads for detecting thread motion during each sewing stitch cycle. Encoder means is operatively associated with the sewing machine for creating a predetermined constant number of sensor means sampling signals for each stitch cycle of the sewing machine, and circuit means is electrically connected to the sensor means and encoder means for detecting stitch defects during the formation of potentially defective stitches.
Stitch quality monitoring system - 2009
By Theodore J. Stokes, Matthew Paul Sherman, Kenneth Mark Eubanks, Paul Truman Statler, Joseph W. Bauman
A stitcher is provided that includes a needle configured to place stitches in a fabric that is moved therethrough. The stitcher includes a sensor positioned below the fabric to monitor stitches placed in the fabric. A microcontroller is provided configured to receive data from the sensor and, based on such data, to compare one or more attributes of the monitored stitches with one or more predetermined parameters relating at least one attribute of the fabric. The predetermined parameter may be either hardcoded inn the microcontroller or input by a user of the stitcher prior to beginning operation of the machine. When the attributes of the monitored stitches fall outside of the predetermined parameters, the microcontroller initiates notification of the user.